## Slide 1: Smart Networks and Service Orchestration
SDN – Performance monitoring
Project 3
Politecnico di Milano, May 30th 2020
Project-Team 8

## Slide 2: Outline
Introduction
Tuned frequency and optical set point
Tx and Rx power
Bit error rate (BER)
Optical channel quality metrics
Addictional functions

## Slide 3: Introduction
The aim of the project was to parse XML responses in order to get some performance metrics or parameters.
Requests: Netconf queries to the selected device
Responses: Xpath filtering on the received XML response

## Slide 4: Requests
<get-config>
We used the function .get_config(), called on the established connection to obtain the list of all the interfaces of the device.
<get-pm-data>
We used the function .dispatch(), to make a custom rpc call since get-pm-data is not a standard call but an ADVA-AOS one. To perform those requests we also had to specify namespaces and the <target-entity> tag containing an xpath query to filter the pm-data.
<get>
We used the function .get(), called to the established connection to obtain tuned frequency and optical set point for each interface.

## Slide 5
Get the XML response object
Parse the string with Xpath expressions to get the data
Print the data
Responses

## Slide 6: Tuned frequency and optical set point
interface_filter = ''' <managed-element> <interface> <name>''' + interface_name + '''</name> <physical-interface/> </interface> </managed-element> '''
With this XML filter we get information about the interface specified in the variable «interface_name»
info_filter = """//*[name()=$tag]"""
Than we use this Xpath filter to obtain the value of associated to that tag. In this case we search for <tuned-frequency> and/or <opt-setpoint>

## Slide 7: Sample output
Getting tuned-frequency and opt-setpoint... ---------------------------------------------------------------------------------------------------- Getting frequency and/or power... ==================================================> 1/2/n1 <================================================== INFO:ncclient.operations.rpc:[host 10.11.12.19 session-id 28] Requesting 'Get' INFO:ncclient.transport.ssh:[host 10.11.12.19 session-id 28] Sending: #407 <?xml version="1.0" encoding="UTF-8"?><nc:rpc xmlns:nc="urn:ietf:params:xml:ns:netconf:base:1.0" message-id="urn:uuid:77d0 a58d-9969-4b39-9ee3-fc497ba57ebe"><nc:get><nc:filter type="subtree"><managed-element> <interface> <name>1/2/n1</name> <physical-interface/> </interface> </managed-element></nc:filter></nc:get></nc:rpc> ## INFO:ncclient.transport.ssh:[host 10.11.12.19 session-id 28] Received message from host **************************************************************************************************** tuned-frequency for 1/2/n1 interface: 196000000 **************************************************************************************************** opt-setpoint for 1/2/n1 interface: 11 ****************************************************************************************************

## Slide 8: Tx and Rx power
rpc = ''' <get-pm-data xmlns="http://www.advaoptical.com/aos/netconf/aos-core-pm" xmlns:me="http://www.advaoptical.com/aos/netconf/aos-core-managed-element" xmlns:fac="http://www.advaoptical.com/aos/netconf/aos-core-facility" xmlns:eth="http://www.advaoptical.com/aos/netconf/aos-core-ethernet"> <target-entity>/me:managed-element[me:entity-name="1"]/fac:interface[fac:name="'‘’
+ interface_name + '''"]/fac:physical-interface/fac:lr-phys''' + m + '''-optical</target-entity> <pm-data> <pm-current-data/> </pm-data> </get-pm-data> '''
mt_filter = '''//*[name()='mon-type']'''
We created the rpc filter to obtain data about transmitted and received power of all the interfaces. Then, using the mt_filter, we obtained a list of all <mon-type> tags present in that interface. From that list we had to select only tx and rx data. To get the actual numeric value we had to access the tag <mon-val>.

## Slide 9: Sample output
Getting transmitted and received power... ---------------------------------------------------------------------------------------------------- INFO:ncclient.transport.ssh:[host 10.11.12.19 session-id 37] Received message from host ==================================================> 1/2/n1 <================================================== **************************************************************************************************** Info for acor-pmt:interval-indefinite: acor-factt:opt-rcv-pwr Value: -13.9 **************************************************************************************************** Info for acor-pmt:interval-indefinite: acor-factt:opt-trmt-pwr Value: 1.1 **************************************************************************************************** Info for acor-pmt:interval-15min: acor-factt:opt-rcv-pwr-lo Value: -13.9 **************************************************************************************************** Info for acor-pmt:interval-15min: acor-factt:opt-rcv-pwr-mean Value: -0.1 **************************************************************************************************** Info for acor-pmt:interval-15min: acor-factt:opt-rcv-pwr-hi Value: 0.0 **************************************************************************************************** Info for acor-pmt:interval-15min: acor-factt:opt-trmt-pwr-lo Value: -45.7 **************************************************************************************************** Info for acor-pmt:interval-15min: acor-factt:opt-trmt-pwr-mean Value: -9.7 **************************************************************************************************** Info for acor-pmt:interval-15min: acor-factt:opt-trmt-pwr-hi Value: 1.1 ****************************************************************************************************

## Slide 10: Bit error rate (BER)
mt_filter = '''//*[name()='mon-type']'''
We created the rpc filter to obtain data about the BER of all the interfaces (if available). Then, using the mt_filter, we obtained a list of all <mon-type> tags present in that interface. From that list we had to select only data related to BER. To get the actual numeric value we had to access the tag <mon-val>.
rpc = ''' <get-pm-data xmlns="http://www.advaoptical.com/aos/netconf/aos-core-pm" xmlns:me="http://www.advaoptical.com/aos/netconf/aos-core-managed-element" xmlns:fac="http://www.advaoptical.com/aos/netconf/aos-core-facility" xmlns:eth="http://www.advaoptical.com/aos/netconf/aos-core-ethernet"> xmlns:otn="http://www.advaoptical.com/aos/netconf/aos-domain-otn"> <target-entity>/me:managed-element[me:entity-name="1"]/fac:interface[fac:name="'‘’
+ interface_name + '''"]/fac:logical-interface/eth:ety6</target-entity> <pm-data> <pm-current-data/> </pm-data> </get-pm-data> '''
NOTE: We noticed that BER data were associated only to client logical interfaces (c1 or c3)

## Slide 11: Sample output
Getting signal BER... ---------------------------------------------------------------------------------------------------- Getting bit error rate... ============================================> 1/2/c1/et100 <=============================================== INFO:ncclient.transport.ssh:[host 10.11.12.23 session-id 28] Received message from host **************************************************************************************************** Info for acor-pmt:interval-indefinite: acor-factt:fec-ber Value: 0.0 **************************************************************************************************** Info for acor-pmt:interval-15min: acor-factt:fec-ber-mean Value: 0.0 ****************************************************************************************************

## Slide 12: Optical channel quality metrics
mt_filter = '''//*[name()='mon-type']'''
We created the rpc filter to obtain data about optical channel performance metrics of all the interfaces (if available). Then, using the mt_filter, we obtained a list of all <mon-type> tags present in that interface. From that list we had to select only data related to optical channel performance metrics data. To get the actual numeric value we had to access the tag <mon-val>.
NOTE: We noticed that those data were associated only to network logical interfaces (n1 or n2)
rpc = ''' <get-pm-data xmlns="http://www.advaoptical.com/aos/netconf/aos-core-pm" xmlns:me="http://www.advaoptical.com/aos/netconf/aos-core-managed-element" xmlns:eq="http://www.advaoptical.com/aos/netconf/aos-core-equipment" xmlns:fac="http://www.advaoptical.com/aos/netconf/aos-core-facility" xmlns:otn="http://www.advaoptical.com/aos/netconf/aos-domain-otn"> <target-entity>/me:managed-element[me:entity-name="1"]/fac:interface[fac:name=«’‘’
+ interface_name + '''"]/fac:logical-interface/optical-channel</target-entity> <pm-data> <pm-current-data/> </pm-data> </get-pm-data> '''

## Slide 13: Sample output
Getting SNR, q-factor and/or group delay... INFO:ncclient.transport.ssh:[host 10.11.12.19 session-id 38] Received message from host ******************************************************************************* Info for acor-pmt:interval-indefinite: adom-oduckpat:signal-to-noise-ratio Value: 13.1 ******************************************************************************* Info for acor-pmt:interval-indefinite: adom-oduckpat:differential-group-delay Value: 1 ******************************************************************************* Info for acor-pmt:interval-15min: adom-oduckpat:signal-to-noise-ratio-lo Value: 0.0 ******************************************************************************* Info for acor-pmt:interval-15min: adom-oduckpat:signal-to-noise-ratio-mean Value: 10.6 ******************************************************************************* Info for acor-pmt:interval-15min: adom-oduckpat:signal-to-noise-ratio-hi Value: 13.2 ******************************************************************************* Info for acor-pmt:interval-15min: adom-oduckpat:differential-group-delay-lo Value: 0 ******************************************************************************* Info for acor-pmt:interval-15min: adom-oduckpat:differential-group-delay-mean Value: 0 ******************************************************************************* Info for acor-pmt:interval-15min: adom-oduckpat:differential-group-delay-hi Value: 2 ******************************************************************************* Info for acor-pmt:interval-indefinite: adom-oduckpat:q-factor Value: 12.8 *******************************************************************************
Info for acor-pmt:interval-15min: adom-oduckpat:q-factor-lo Value: 0.0 ******************************************************************************* Info for acor-pmt:interval-15min: adom-oduckpat:q-factor-mean Value: 10.4 ******************************************************************************* Info for acor-pmt:interval-15min: adom-oduckpat:q-factor-hi Value: 12.8 *******************************************************************************

## Slide 14: Addictional functions
To better analyze metrics we built two addictional functions which periodically call all the previously explained functions.
def periodic_requests(): """Periodically iterates all the previous requests"""
def periodic_variable_requests(): " Periodically iterates all the previous requests, with the possibility to change host or stopping the requests at each iteration """
Since we may need to check all the interfaces present in a host, we also built an addictional function which allows us to do so.
def get_interfaces(): """Request all the interfaces """

## Slide 15: THANKS